A = 1, a = 1, B = 0, b = 1, beta = 2
c predicted as ~3.5
Actual stable value ~18
Reach x = -10 at t = 0.29

Set A = 2, use same profile
Something kinda fucked up happened
Took 5x as long to compute
Wave actually looks pretty much constant in speed
Reaches edge at around t = 2.4
Reaches top around t = 4.8
c ~= 4.17
Equations predict c ~= 5.35

Keep A = 2, use a profile generated for this setting
Basically same, straight line plotted
Gets a slightly faster time, but that might be just the start being a bit fast
Takes same amount of time (5min)
Wait, did I not save the parameters properly? No wonder it took longer, the grid was too big.
Though I don’t know what that means for the neurons on it, since it plots in 3D as a straight wave of constant speed,
and since the wave looped across x-distance 20 exactly once in 20k firing events, that means it fired 100 times every 0.1, which was the intended spacing of neurons. Did I somehow underpopulate the neuron grids?

A = 2, actually on 200x100 grid now
(Was prev. on 500x250)
Took 100 seconds
Looks like the A = 1 case
Basically the same speed too…

Try it again, dz = 1
Shouldn’t do anything, in theory
Didn’t do anything!

Double grid size, halve spacing, still use 200x100 input
Well, the wave does look straighter, and slower, but it gets confused about the looping.

Set to 500x250, grid appropriately shrunk down, still use 200x100 input
This gets the straight-wave behaviour seen earlier

Same grid, but with a proper 500x250 input
Now looks more like the originals, with a straight wave speeding up and going at high speed.

Dropping down to 500x100 grid, 500x100 input
Pretty much the same, though with more spread in the neuron firing times

...Was I also generating input profiles with A = 1 still? Or did I look at the wrong open file?
Seems like I looked at the wrong file.

When running with an input profile instead of computing the initial values, I suppress a bunch of initialisation functions for the arrays. These arrays start out full of zeroes, so if I use an input profile with fewer neurons than the program expects, the remaining neurons are effectively stacked up at (0, 0).
Since their (v, s) = (0, 0) also, and I’ve had the wave starting at x = 0 then looping around exactly once, I’ve by luck avoided triggering off all those hidden neurons.
This means that these neurons are contributing nothing to the prior dynamics since they never fire. Therefore, the only thing that’s actually changing is the fact the system is reading a grid spacing that’s smaller than it actually is. That’s only used outside of initialisation when it comes to propagating signals – specifically, it’s beta*dx*dy as the factor by which all signals are multiplied, to conserve the amount of signal sent.
I was expecting to be using 1*0.1*0.1 = 0.01 but was actually using 1*0.04*0.04 = 0.0016. Copying the code into the command line, it looks like those should be the values put out. The difference is a factor of 6.25, and was enough to get back to roughly what I thought the wave should look like.

Tried generating the wave speed with absolutely everything broken down into the basic components, forward Euler everything, and it still agreed with the equations.

Since the 2D wave is uniform along the y-coordinate, and the gaussian function separates in the x and y coordinates so that the input along the wave front is just a scaling coefficient for the weighting function in the x-dimension, I should be able to project everything down to 1D and get the same results just by changing A.
Don’t need to worry about scaling a, since the a/c thing is from x = ct, and we’re using x instead of t here.

sqrt(2pi) ~= 2.507
Putting A = 2.507 in 1D gives similar wave effects as seen in 2D. That is, the wave speeding up to reach x = -10 at around t=0.6. Given that a = 1, this is the factor we expect should give us identical behaviour. (Initial speed around c = 6 before speeding up to c = 18)

Putting A = 1 gives a less pronounced-looking speed-up, but still takes it to x = -10 by t = 1.75. A speed of around 5.7, ignoring the acceleration period. The difference in speed-up severeness may be due to the underlying initial conditions (expecting A = 1 using 2D equations). Remember that we expect c = 3.48.

Putting A = 0.4 ~= 1/2.507 gives a wave that starts with a speed of 2.7 but slows down and fails after 36 spikes.

A = 0.5: initial c = 2.7, also fails
A = 0.6: slows down slightly at start, c = 2.4 in long-run
A = 0.7: no visible speed change, c = 3.3
A = 0.8: c = 4.17
A = 0.75: c = 3.76
A = 0.73: c = 3.60
A = 0.72: c = 3.52
A = 0.715: c = 3.50

That’s close enough.
We already know about a sqrt(2pi) difference between 1D A and 2D A. 1/0.715 ~= 1.40… that’s very close to sqrt(2) ~= 1.414.
If that’s the true factor difference, we would get A = 0.707 as our matching value; however, I’ve already established that the wave should travel slightly slower than the continuum limit on a discrete grid, with coarser grids being slower.

Overall this gives us a 2*sqrt(pi) difference to account for. Can verify this holds in 2D by multiplying an above result by 2.507 and seeing it still looks the same.

0.715/2.507 ~= 0.2852
Set A = 0.2852, 500x100 grid, 500x100 input
Didn’t set neuron count high enough to actually get all the way around but the speed comes out as about c = 3.44. So roughly correct.

So. The value of A I put in to the program gets multiplied by 2sqrt(pi). Or the value in my equations somehow got divided by that amount.
For security, I should really screw around with a as well. Maybe also check that this all applies when A isn’t meant to be 1, since that is a special number.

A = 2 in start profile and in code parameters, 500x1
Target is c = 5.35
Reaches x = -10 at t = 0.755, for an actual speed of around 13
Did have a speed-up period, though.

Now try dividing by 2sqrt(pi) ~= 3.545

A = 0.564 in code
c = 2.1, slowed down from original

Wait no, already implicitly multiplied by sqrt(2pi), so only need to divide by sqrt(2)
i.e. run for A = sqrt(2)

A = 1.41
c = 9? Not expected. Has some speed-up at the start.
Well, we remember from before that A = 1 gave a speed of around 5.7.
With the new start profile it’s a speed of around 5.9.

A = 0.9: c = 5.1
A = 0.93: c = 5.33
Also note that there isn’t spontaneous extra wave generation, but the subsequent loops are fast enough that they ride the latent excitation and get faster and faster.

This time, it isn’t obvious what the factor might be. Or rather, perhaps it was a coincidence that the factor seemed obvious before?
Well, it would seem to be a non-linear defect…

A = 1, a = 2, 500x100, 25000 spikes
Also setting v_r = -10 to avoid echo-y things happening
Target is c = 6.97
Starts off slow...er, about c = 10, accelerates to c = 74
Reaches x = -10 at t = 0.1772

A = 2.507, a = 2, 500x1
Reaches x = -10 at t = 0.3358, c = 37. ??? Half as slow as before.
A = 5.014, a = 2, 500x1
Behaviour largely restored. Right, it was only factor sqrt(2pi) because a = 1, it’s actually a*sqrt(2pi).

A = 1: c = 11
A = 0.9: c = 10
A = 0.8: c = 8.3
A = 0.7: c = 6.74
A = 0.715: c = 6.97

Seems like changing a didn’t change the factor by which I needed to change A to get the correct result.
Is it sensible to fiddle with the value of a as well? That feels like something more qualitative.

The fact that the scaling factor a*sqrt(2pi) does work is a sign that the integration across the wave front is somehow correct.

A = 2 in profile, A = 0.93 in parameters, a = 2
As expected, this gets the correct speed.

Should I screw about with beta too?

A = 1, a = 1, beta = 3
Expected c = 4.18
Set A = 0.715 in code again
Get c = 5.63…
Try 0.715 * 2/3 ?
A = 0.476: c = 2.41
A = 0.6: c = 4.23
A = 0.577 (= (1/3)^0.5): c = 3.93
A = 0.59: c = 4.08

0.6 was close enough, really. Near to the inverse of the square root of 3…

A = 1, a = 1, beta = 4
Expected c = 4.72
A = 0.5: c = 4.21
A = 0.6: c = 5.9
A = 0.52: c = 4.58
A = 0.54: c = 4.90
A = 0.53: c = 4.75

A = 1, a = 1, beta = 5
Expected c = 5.17
1/sqrt(5) ~= 0.447
A = 0.45: c = 4.42
A = 0.5: c = 5.54
A = 0.48: c = 5.10
A = 0.485: c = 5.21

Really I’d like to see what happens when beta = 1, but my current programs aren’t set up for that.
But what if beta = 1.001?
A = 1, a = 1, beta = 1.001
Expected c = 2.50
A = 1: c = 2.50

So it seems the error term has no dependence on a (or it’s cancelling out somewhere),
and when A = 1 it is equivalent to multiplying A by sqrt(2*pi*beta).

With that in hand, now to figure out what happens as A increases.

A = 2, a = 1, beta = 1.001
Expected c = 3.82
A = 2: c = 6.49
A = 1: c = 2.57
A = 1.4: c = 4.17
A = 1.3: c = 3.77
A = 1.32: c = 3.89
A = 1.31: c = 3.83	2/1.31 = 1.53

A = 3, a = 1, beta = 1.001
Expected c = 4.83
A = 3: c = 10.3
A = 1.5: c = 4.63
A = 1.6: c = 5.0
A = 1.56: c = 4.88
A = 1.55: c = 4.83	3/1.55 = 1.93

A = 4, a = 1, beta = 1.001
Expected c = 5.68
A = 4: c = 14
A = 1.7: c = 5.46
A = 1.75: c = 5.68	4/1.75 = 2.29

(Just checked, while B = 0, setting b = 1 or b = 10 didn’t change anything.)

Post-Christmas recap: it seems confirmed that the problem is in the code. What did I find out previously about this problem?
- Waves are travelling too fast in the computer model
- Restricting to excitatory-only, I have the variables A, a, beta
  - A: magnitude of excitatory broadcast
  - a: standard deviation of excitatory broadcast curve
  - beta: rate of synaptic value decay
- I can translate from 2D to 1D straight waves by multiplying by a*sqrt(2pi) (?) and the behaviour remains the same
  - Consistent across grid spacing too, IIRC
- When A = 1, I can compensate for the error by dividing A by sqrt(2*pi*beta)
  - If I’ve reduced to 1D, then dividing by sqrt(2*pi) cancels out and I just divide by sqrt(beta)
  - Note that this doesn’t seem to have a dependence on a
- When A != 1, the error formula is different
  - For starters, it seems inappropriate to try to tweak A as the “solution” to errors dependent on A in the first place.
  - Since the output is 1 value and the input is 3 values, I have some freedom in which variables I tweak to “fix” the errors.

Double-checking my knowledge with some 500x1 simulations:

Computer input: A = 1, a = 1, beta = 1.001
Results in c = 2.63, though admittedly I’m not using the correct starting conditions
Intended value: c = 2.50
Basically correct, so this is the sqrt(2*pi) error cancelling out

A = 1, a = 2, beta = 1.001
Intended value: c = 5.00
Result: c = 5

A = 1, a = 3, beta = 1.001
Expecting c = 7.50
Result: c = 7.56

Wave speed being a linear function of a should be expected, and independent of everything else, as it’s determining the spatial scale. Or should it? The Gaussian curve conserves area, so doubling a means the peak signal strength is halved. Though if the wave travels twice as fast, you get twice as many signals… so it cancels out. Yes, linear is appropriate.
Wait, wasn’t my correction term supposed to be a*sqrt(2*pi) when moving from 2D to 1D? What happened to the a? Because in 2D we integrate the Gaussian twice instead of once without adding in a second pre-factor. So maybe there is an error dependent on a, and it’s self-cancelling.

Is all this going to get me closer to fixing the problem, though?

Where could the error be hiding?
- Root-finding: Newton-Raphson is generic, and if I’d coded it wrong I feel like that would’ve been evident by now. Could there be an error in the equations for v(t) and dv/dt themselves?
  - Hm, wouldn’t these calculations break if I put beta = 1 in? Have I really not tested the beta = 1 version of this program yet? How was I running it before?
  - Somehow beta = 1 causes every neuron to fire at once. ...I feel like this is something to chase up later.
  - Anyway, equation for v(t) is what I have written down in my running review, and dv/dt is literally just the ODE statement once you’ve solved s.
- Updating s: in generic.postclean, I have
  - synapse_d[n] *= e**(-synapse_decay * fastest_time_d)
  - synapse_d[n] += Control.c.connection_weight(distance)
  - The former is simply the solution to ds/dt = -beta*s, that being s(t) = s_0 * exp(-beta*t).
  - The latter adds the value beta * density_factor * strength * gaussian_curve(distance, sigma).
    - density_factor is dx, or dx*dy, or dx*dy*dz, whichever is relevant. I have dy = 1 for now so it doesn’t change between 1D and 2D.
    - Strength is just A
    - device_gaussian is a generic implementation of a normal curve, no extra coefficients.
  - That sure looks like it was the planned form. And as density_factor approaches zero, you should tend towards the integral I used.

You know, I’ve tried looking before, and not spotted anything. I shouldn’t really expect look harder to work either. So how do I go about debugging it?

If I substitute device_gaussian for a linear function that hits zero after some distance, that should at least make it easier to tell what should happen. Although, I could also go through the log files directly, right? I save that output for a reason, even if it’s just the firing times.

First of all, I need to set up a test case where things are known to go wrong.

A = 2, a = 1, beta = 1.001
Expected: c = 3.82
Actual: c = 6.45

Wait no, I don’t want to be calculating all these exponentials, do I? Make an alt version of the program where both the connection function is linear (Starts at A, gradient is A/a?) and the decay of s is linear (gradient is beta?) until it reaches zero.
What would this sort of travelling wave look like? Probably just need to establish the relation between the firing neuron and the next neuron along, since it’s linear. v(t) equation is still exponential, mind you. Should I change that too? Eh, maybe this was a bad idea, I should just go back and do the step-by-step properly. Or when I’m less tired.

Discussed with Kyle making a time-stepping solver to go side-by-side. He suggested Runge-Kutta, I suggested Forward Euler.

Import functions from existing modules, or rewrite from scratch? Well, some are GPU-only, while others are things like importers that it would be foolish not to reuse.

Set up a Forward Euler version, and it’s producing essentialy the same results as the fancy version. So wherever the issue is, it’s within something I’m importing. Which is…
- Importing data from the initial profile
- Reading values from .txt files
- Distance calculation
- Connection weight calculation
Rewrote distance as just dx * index difference, no change.
Rewrote gaussian, still the same

Hm, test on different numbers?
Set beta = 2, now there’s difference.
Put back the original connection_weight and… hm, now it matches the fancy one.
Ooh, wait, I forgot to multiply signal strength by beta in the new one. Hrm, now it matches again…
So, does this mean the mistake is in theory?

Tried 3/3/2 also. All the same.